CLASS B PRE-TRIP INSPECTION

“Chris’ Checklist”

- Front of Vehicle

  - “Standing Straight and Tall”

  - Upper Lights and Reflectors

    - Present, clean and not broken, color correct

  - Windshield/Wipers

    - Clear, No Cracks, Cleanliness, Condition

  - Grill

  - Lower lights/Reflectors

    - Present, clean and not broken, color correct

  - Bumper

  - Underneath Cab

    - Fluid leaks, Front axle condition

- Engine Compartment

  - Fluid Checks-Verbally state how to check each fluid type

    - Oil, Coolant, Power steering, Window washer

  - Belts - Water pump, Alternator, Power steering, Air compressor

    - Check Deflection (tightness), Condition/Wear, Alignment

  - Fluid Leaks

    - Oil, Fuel, Power steering, Coolant

  - Hoses

    - Check for Wear, Age, Clamps, Condition (bulges, cracks)

  - Wiring and Air Lines

    - Check for Wear (abrasion), Bare wires, connections secure

  - Air Cleaner and Ducting

    - Clean, Secure (clamps), Leaks

  - Exhaust System

    - Check entire system for Leaks, Clamps Secure

Notes: ____________________________________________________

__________________________________________________________

__________________________________________________________

__________________________________________________________

- Front Suspension

  - Frame (front)

    - Check for: Cracks, Damage, Extra holes, Bolts missing, Welds

  - Axle

    - Bent or Damaged? Secure to Frame

  - Springs/Shocks

    - Properly attached to frame and axle, Damage?  Vehicle out of service if more than 25%  of springs are broken

    - Shocks secure to frame and axle and not leaking

  - Steering Components – Steering Shaft, Steering Box, Pitman, Steering arm, Tie rod

    - Check each component for: Secure, Missing bolts, Damage and Alignment

  - Front Brakes

    - Check air lines for damage and rubbing against frame

    - Brake chamber secure and undamaged?

    - Slack adjuster (<90 degrees) Push rod (<2” travel)

    - Drums – cracks/damage, Linings (thickness must be greater than 1/4”)

- Tires/Wheels

  - Tires

    - Inflation-check with a gauge.

    - Cap present?

    - Condition/Damage

      - inside, top, outside

    - Tread depth (4/32”)

  - Rims

    - Check for Cracks, Damage, Welds

  - Lug Nuts

    - Check Tightness (rust trails), Missing nuts?

  - Axle Hub Seal

    - Check for leaks and fluid level (Inside and outside hub)

- Side of Vehicle

  - Passenger Doors

    - Secure, Aligned, Do they lock?

  - Windows/Mirrors

    - Check for damage, Securely attached, Aligned? Windows roll up and down

  - Cargo

    - Secured, Compartment doors closed

  - Battery/Battery Compartment

    - Make sure box is securely attached to the frame

    - Batteries secure, Clean (corrosion), Connections tight?

  - Fuel Tank

    - Cap on and no leaks

    - Electrical connections secure

    - Check fuel level (check against fuel gauge during “in-cab check”)

  - Reflective Triangles

    - Condition, Location/Set up

  - Frame (mid area)

    - Cracks, Damage, Extra holes, Bolts missing, Welds

  - Drive Shaft

    - Secure, Straight, Clear

  - Exhaust System

    - Leaks, Clamps, Secured to frame

- Rear Axle

  - Frame (rear)

    - Cracks, Damage, Extra holes, Bolts missing, Welds

  - Springs/Shocks

    - Properly attached to frame and axle, Damaged?  Out of service if more than 25%  are broken

    - Shocks secure to frame and axle and not leaking

  - Rear Brakes

    - Same as front – Check Air lines, Brake chamber, Slack adjuster (<90°), Push rod (<2” travel), Drums (cracks), Linings (wear <1/4”)

  - Differential

    - Check for Leaks, Damage, Securely attached to frame

- Rear Tires/Wheels

  - Rims

    - Cracks, Damage, Welds

  - Lug Nuts

    - Tightness, Missing?

  - Axle Hub Seal

    - Leaks

  - Tires (Duals)

    - Inflation (gauge), Cap, Condition, Tread depth (2/32”),  Equal size and type, check for adequate space between tires and objects between duals

- Rear of Vehicle

  - Upper Lights/Reflectors

    - Present, clean and not broken, color correct

  - Lift Gate

    - Secure

  - Mud Flaps

    - Check for Secure, Damage, Dragging or rubbing

  - License Plate

    - Lighted, Secure

Notes: ____________________________________________________

__________________________________________________________

__________________________________________________________

__________________________________________________________

__________________________________________________________

__________________________________________________________

__________________________________________________________

- In Cab Check

  - Clutch/Gearshift

    - Clear, Able to shift all gears, Depress clutch

    - Automatics must shift through all gears

  - Start engine and check all gauges for correct operation.  Verbally give status of each gauge:

    - Oil pressure, Temperature, Ammeter/Voltmeter, Air gauges, Tachometer, Speedometer, Auxiliary gauges (identify each gauge and describe)

  - Steering Play/Horn

    - With engine on, move steering wheel back and forth to check for play: 10° max. Visually check by looking at front tire

    - Check air and electrical horns

  - Mirrors/Windshield/Wipers

    - Mirrors adjusted, clean and free of obstructions

    - Windshield clean and free of obstructions

    - Wipers, Washer operational

  - Interior/Dash Lighting

    - Check: Right/Left turn, 4 way flashers, High beam, gauge lamps, dome lights

  - Heater/Defroster

    - Fan and vents operational

  - Safety Items

    - Seat belts, Fire extinguisher (if required)

    - Electrical fuses (if required)

- Air Brake Test

  - Cut-out

    - Start engine and allow pressure to build until compressor stops.  Note pressure (around 125 PSI)

  - Applied pressure

    - Fully charge air system and shut off engine, release parking brake, hold service brake down (< 3 PSI/min)

  - Cut-in

    - Start engine

    - Pump down brake pressure until air compressor cuts in (>85 PSI)

  - Low Pressure Warning

    - Pump down brakes until audible and visible devices activate (60-75 PSI)

  - Parking Brake Test

    - Roll forward less than 5 MPH and apply parking brake.  Should stop smoothly

Notes: ____________________________________________________

__________________________________________________________

__________________________________________________________

__________________________________________________________

__________________________________________________________

__________________________________________________________

__________________________________________________________

- Buses (Passenger endorsement)

  - Passenger compartment cleanliness, nothing in the isles.

    - Tools and equipment secure

    - Check for any Haz-Mat

  - Seats

    - Check condition, secure to floor

    - 1 per rider

Check emergency exits, side windows and roof.

  - Check entry way, steps, handholds.

Notes:_______________________________________________________________________________________________________________

__________________________________________________________

__________________________________________________________

__________________________________________________________